Tender specification text

Multiple casing end seal

MAM-R (red)

Multiple casing end seal for cable conduits with several carrier pipes or cables

Multiple casing end seal with welded carrier pipe sleeves to be delivered and installed over the cable conduit and the carrier pipes/cables with tightening straps at the end of the cable conduit according to the manufacturer’s specifications.

Product:

DDL Multiple Casing End Seal MAM-R

DDL GmbH, 73249 Wernau / N.

or equivalent

Outside diameter of the casing pipe/cable conduit

(including potential casing):	            		DN ….………….………	OD ………….…..……….. mm

Outside diameter of carrier pipe 1

(including potential casing):			DN ….………….………	OD ………….…..……….. mm

Outside diameter of carrier pipe 2

(including potential casing):			DN ….………….………	OD ………….…..……….. mm

Position of carrier pipe 1

in the casing pipe/cable conduit			centric …………………	according to drawing: ………..

Position of carrier pipe 2 / cable

in the casing pipe/cable conduit			clock position…………	according to drawing: ………..

Material:

Seal:			Thermoplastic elastomer

Tightening straps: 	Stainless steel

Amount of seals:								            Pcs. ………….

Unit price: ………………….. €	            Total price: .……….…….……€