Tender specification text

Building entry

Against pressing water

Stainless steel version

Lu-SW  VA

Seal for pipe penetrations against pressing water, stainless steel V4A / AISI 316Ti, split version

Seal insert consisting of an elastomer sealing ring and segmental pressure plates for sealing individual pipelines going through building walls and ceilings

to be delivered and installed into the annulus between wall sleeve/core-drilled hole and the carrier pipe supposed to be led through according to the manufacturer’s installation instructions.

Product:

DDL Building entry Lu-SW VA

DDL GmbH, 73249 Wernau / N.

or equivalent

Outside diameter of the carrier pipe (including

potential factory coating):	            			 DN ….………	  	OD …………… mm

Inside diameter of the wall sleeve or core-drilled hole:				ID ….….…...… mm

Pressure level:									     20 mWS / 2 bar

Material

- Sealing ring:		EPDM, without DOP/DEHP plasticizers (split)

- Pressure plates:	Polyamide (glass fiber reinforced)

- Screws:		Stainless steel V4A/AISI 316Ti

Model/name:								            Lu-SW VA / DN…..…

Amount of seal inserts:								  	    Pcs. …..…

Unit price: ……………€	   	   Total price: ………………..€