Tender specification text

Wall collar

Seal against pressing water

MK-KG

Wall collar KG for sealing pipes against pressing water

Wall collar consisting of an elastomer sealing lip and two tightening straps which are put into the grooves of the wall collar and mounted on the pipe. To seal single pipelines led through building walls or ceilings against pressing water.

Product:

DDL Wall Collar MK-KG

DDL GmbH, 73249 Wernau / N.

or equivalent

Outside diameter of the pipe:            			    DN ….………	 OD …………… mm

Pressure level:								         against pressing water

Materials:

- elastomer sealing lip:		EPDM, without DOP/DEHP plasticizers

- tightening straps:		Steel with aluminum and zinc finishing

Model/Name:							           		 MK-KG / DN …..……

Amount of wall collars:								Pcs. …………..………

Unit price: ……………€	   	   Total price: ………………..€