Tender specification text

Annular seal

Compact seal insert, split

Single sealing, stainless steel version

Layered-ring system

PS KombiFlex ED-G

Compact seal insert adaptable to the carrier pipe dimension (layered-ring system) on site, single sealing, split, stainless steel version V2A/AISI 304, for sealing pipe penetrations.

Compact seal consisting of an elastomer sealing ring and stainless steel pressure plates for sealing individual pipelines going through building walls and ceilings

to be delivered and installed into the annulus between wall sleeve/core-drilled hole and the carrier pipe supposed to be led through according to the manufacturer’s installation instructions.

Product:

DDL Compact Seal PS KombiFlex ED-G

DDL GmbH, 73249 Wernau / N.

or equivalent

Outside diameter of the carrier pipe (including potential factory coating):			20 – 65 mm

Inside diameter of the wall sleeve or core-drilled hole:					  ID 100 mm

Pressure level:									          Single sealing

Material

- Sealing ring:	EPDM, 30 mm, without DOP/DEHP plasticizers (split)

- Steel frame:	Stainless steel V2A/AISI 304 (split)

- Screws:	Stainless steel V2A/AISI 304

Model/name:								PS KombiFlex ED-G  DN 100

Amount of seal inserts:								  Pcs. ………..………

Unit price: ……………€	   	      Total price: ……………..€