Tender specification text

Annular seal

Multiple-penetration compact seal insert

Single sealing, stainless steel version

PS Multiple Penetration ED

Compact seal insert with a steel frame for sealing multiple pipe penetrations, single sealing, stainless steel V2A/AISI 304

Compact seal consisting of an elastomer sealing ring and stainless steel pressure plates for sealing multiple pipelines going through building walls and ceilings

to be delivered and installed into the annulus between wall sleeve/core-drilled hole and the carrier pipes supposed to be led through according to the manufacturer’s installation instructions.

Product:

DDL Annular Seal PS Multiple Penetration ED

DDL GmbH, 73249 Wernau / N.

or equivalent

Outside diameter of the carrier pipe

(including potential factory coating):

……..X carrier pipe 1	DN ….………	OD …………… mm

……..X	carrier pipe 2	DN ….………	OD …………… mm

……..X carrier pipe 3	DN ….………	OD …………… mm

……..X	carrier pipe 4	DN ….………	OD …………… mm

Inside diameter of the wall sleeve

or core-drilled hole:								ID ….….…...… mm

Pressure level:									        Single sealing

Material

- Sealing ring:	EPDM, 30 mm, without DOP/DEHP plasticizers

- Steel frame:	Stainless steel V2A/AISI 304

- Screws:	Stainless steel V2A/AISI 304

Model/name:						     PS Multiple Penetration ED /  DN …...…

Amount of seal inserts:							  	   	 Pcs. ……..

Unit price: ……………€	   	   Total price: ……………..€