Tender specification text

Annular seal

Compact seal insert

Single sealing, stainless steel version

Pipe-Seal ED

Compact seal insert with a steel frame for pipe penetrations, single sealing, stainless steel V2A/AISI 304

Compact seal consisting of an elastomer sealing ring and stainless steel pressure plates for sealing individual pipelines going through building walls and ceilings

to be delivered and installed into the annulus between wall sleeve/core-drilled hole and the carrier pipe supposed to be led through according to the manufacturer’s installation instructions.

Product:

DDL Compact Seal Pipe-Seal ED

DDL GmbH, 73249 Wernau / N.

or equivalent

Outside diameter of the carrier pipe (including

potential factory coating):	            			 DN ….………	  	OD …………… mm

Inside diameter of the wall sleeve or core-drilled hole:				ID ….….…...… mm

Pressure level:									         Single sealing

Material

- Sealing ring:		EPDM, 30 mm, without DOP/DEHP plasticizers

- Steel frame:		Stainless steel V2A/AISI 304

- Screws:		Stainless steel V2A/AISI 304

Model/name:								       Pipe-Seal ED / DN…..…

Amount of seal inserts:								  	     Pcs.	 ….…

Unit price: ……………€	   	   Total price: ………………..€