Tender specification text

Annular seal

In modular construction, pressure tight up to 50 mWS / 5 bar Stainless steel version

Ring-Seal LU-GT / 50 VA

Modular seal insert with stainless steel screws for sealing pipe penetrations against pressing water

Modular seal consisting of elastomer sealing elements for sealing individual pipelines going through building walls and ceilings pressure tight up to 50 mWS (5 bar)

to be delivered and installed into the annulus between wall sleeve/core-drilled hole and the carrier pipe supposed to be led through according to the manufacturer’s installation instructions.

Product:

DDL Ring-Seal Modular Seal Lu-GT / 50 VA

DDL GmbH, 73249 Wernau / N.

or equivalent

Outside diameter of the carrier pipe

(including potential factory coating):	            		DN ….………		OD …………… mm

Inside diameter of the wall sleeve

or core-drilled hole:								ID ….….…...… mm

Pressure level:										     50 mWS

Material

Elastomer sealing elements without DOP/DEHP plasticizers,

optional material:

- EPDM

- Nitrile

- Silicone

Pressure plates: Polyamide (glass fiber reinforced)

Screws:	Stainless steel

Model/type/name:						  Ring-Seal  Lu-GT ………..…50/VA

Amount of sealing modules per seal insert:				           Pcs./ring …………….

Amount of sealing rings:							    Pcs. ………..……

Unit price/ring: ……………€	    Total price: ……………..€